## Slide 1: Minimum Supply Voltage and Very-Low-Voltage Testing
ECE 7502 Class Discussion
Elena Weinberg
Thursday, April 16, 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Post Silicon Verification
Test
Test

## Slide 3: Low voltage testing
THE IDEA:
ICs with defects more likely to fail at lower voltages
Can we determine a defective chip based on the voltage at which an IC fails?
Idea proposed in [1] in 1993

## Slide 4: Approaches
Very-low-voltage (VLV) testing [1]
MINVDD testing [2]
Low VDD vs. delay correlation metric [4]
Selecting optimal VDD for test [5]

## Slide 5: Challenges for low voltage testing
Time consuming
Scaling  higher impacts from variations
How low is low enough? What is an optimal VDD selection?

## Slide 6: VLV testing [1]
Test chips with very low supply voltage
“Weak” ICs fail when “good” ICs do not
Simple—no design for testability required
Detects resistive shorts and hot carrier effects

## Slide 7: Resistive short
[1] Hao et al, TC’93

## Slide 8
Increased threshold voltage (VT)
Decreased transconductance (proportional to mobility)
Increased substrate current in FET
 oxide degradation
Hot carrier effects
VT shifted 0.3V
[1] Hao et al, TC’93

## Slide 9: Applications [1]
Built-in self test (BIST)
Production test
  Detects weak chips due to resistive shorts
Preventative test  high reliability in field
  In-system test performed periodically (e.g. at power up)
  System degradation detected before failure occurs
Diagnostic test

## Slide 10: VLV results [1]
[1] Hao et al, TC’93

## Slide 11: VLV results [1] (2)
Done in conjunction with
  IDDQ testing, burn-in testing
Detected delay faults
Advantage: simplicity and applicability
Disadvantage: time consuming

## Slide 12: MINVDD testing [2]
Builds on [1]
Determine the minimum supply voltage at which a circuit continues to switch
  Below this VDD, the circuit no longer switches
“Weak” ICs are determined by their minimum supply voltage
  Higher than for “good” ICs
Detects
  Metal shorts
  Gate-oxide shorts
  VT shifts (global and local)
  Tunneling opens
[2] Tseng et al, VLSITS’01

## Slide 13: MINVDD testing [2] (2)
Metal shorts
Gate oxide shorts
^ Significantly higher minVDD for circuits with shorts
VT shifts: larger shift => larger minVDD
  minVDD of good chip should be slightly above VT
Tunneling opens
  Higher delay
[2] Tseng et al, VLSITS’01

## Slide 14: Results [2]
320 Murphy CUTs
(circuits under test)
195 good
116 defective
9 VLV-only
[2] Tseng et al, VLSITS’01

## Slide 15: Low VDD vs. Delay [4]
How to determine limit value with parameter variations?
Popular method: correlate supply voltage reduction to induced change in circuit delay
  Delay variation-dependence with lower VDD not explored
As VDD  VT
 impact of parameter variations on delay
[4] Bota et al, VLSITS’06

## Slide 16: Reduce Test Time for Power Constrained Circuits [5]
Optimal selection of VDD
  Power constraints
  Fastest clock speed
[5] Venkataramani et al, VLSID’13
T = Test clock period
EMAX(test) = Max energy dissipated during vector period
PMAX(func) = Max allowable power obtained from functional simulation
Min VDD is optimum

## Slide 17
[5] Venkataramani et al, VLSID’13
Max allowable power during functional op.
Percentage reduction achieved through proposed method

## Slide 18: Other related techniques
[6] evaluates functionality of SRAM at low VDD
[3] evaluates trade-off between maximum defect coverage and lowest test cost
  “You can test for all of the defects part of the time, part of the defects all of the time but you cannot test for all the defects all of the time!” (Madge et al, TC’04)
  Min VDD testing often used in conjunction with other techniques, much like IDDQ testing

## Slide 19: Conclusion
Low voltage testing techniques are useful as a first step to defect detection, however, they are time consuming and detect a limited number of faults.

## Slide 20: Discussion questions
What are the limitations of min VDD testing?
Could standard min VDD testing be applied to circuit components designed to operate in sub-threshold?
With the sensitivity to variations that nearly all modern circuits experience from scaling, is min VDD testing still effective?
What are some other applications of min VDD or VLV testing? Are there any other ways these techniques could be used in the testing process?
How can we best manage the trade-off between lowest test cost and maximum defect coverage?

## Slide 21: Papers
[1] Hao, Hong, and Edward J. McCluskey. "Very-low-voltage testing for weak CMOS logic ICs." Test Conference, 1993. Proceedings., International. IEEE, 1993.
[2] Tseng, Chao-Wen, et al. "MINVDD testing for weak CMOS ICs." VLSI Test Symposium, 19th IEEE Proceedings on. VTS 2001. IEEE, 2001.
[3] Madge, Robert, et al. "In search of the optimum test set-adaptive test methods for maximum defect coverage and lowest test cost." Test Conference, 2004.
[4] Bota, Sebastiàn A., et al. "Low v/sub dd/vs. delay: is it really a good correlation metric for nanometer ics?." VLSI Test Symposium, 2006. Proceedings. 24th IEEE.
[5] Venkataramani, Praveen, and Vishwani D. Agrawal. "Reducing test time of power constrained test by optimal selection of supply voltage." VLSI Design and 2013 12th International Conference on Embedded Systems (VLSID), 2013 26th International Conference on. IEEE, 2013.
[6] Gottscho, Mark, et al. "Power/capacity scaling: energy savings with simple fault-tolerant caches." Proc. DAC. 2014.

## Slide 22: Paper Map
[1] Hao, H.; …"Very-low-voltage testing …," TC’93.
[2] Tseng, C.; …"MINVDD testing for …," VLSITS’01.
[3] Madge, R.; …"In search of the optimum …," TC’04.
[4] Bota, S.; …"Low v/sub dd/vs. delay: is …," VLSITS’06.
[5] Venkataramani, P.; …"Reducing test time …," VLSID’13.
[6] Gottscho, Mark, et al. "Power/capacity scaling: …,” DAC’14.
[1] Proposed very-low-voltage (VLV) testing
[2] Proposed min VDD testing
[4] Low VDD vs. Delay comparison
[6] More related to sub-VT, but involves low voltage testing
[2] builds on [1]
[5] Optimal selection of VDD
[4] evaluates effectiveness of methodology in [2]
[3] Managing trade-offs in test